C5 C6 (2004-2008) Drive Shaft Nut Torque

Tapping or Scraping Noise From Rear Wheel Area (Replace Wheel Drive Shaft Nut) #07-04-95-001 - (09/26/2007)

Models: 2004-2008 Chevrolet Corvette and 2004-2008 Cadillac XLR
-------------------------------------------------------------------------------
Condition
Some customers may comment on a tapping or a scraping noise coming from the rear wheel area.

Cause
This condition may be due to the torque on the wheel drive shaft nut relaxing over time.

Correction
Replace the left and the right wheel drive shaft nut following the procedure below.

Remove the center cap from the rim.
Remove and discard the wheel drive shaft nut.
Apply LOCTITE™ 272, or equivalent, to the threads of the axle shaft.
Install the nut and tighten to the new specification.
Tighten
Tighten the nut to 215 N·m (160 lb ft).

Install the center cap to the rim.
Important: The vehicle should not be driven for 24 hours following the repair in order to allow the thread lock to cure.
Parts Information
Part Number.....10257766
Description......Nut
Qty................2 (one per side)

Warranty Information: Labor op F9712 0.3 hr.